YEAR

MODEL

NUMBER

MODEL/TYPE

KIT #

STUDEBAKER

6 CYL

1936 - 37

DICTATOR 5A, 6A

627S, SA

CARTER WE

2002

1937

DICTATOR 5A, 6A

371S

CARTER W-1

2015

1938 - 40

DICTATOR COMMANDER

380858 (6-90)

STROMBERG BXOV-26

2037

1938 - 49

COMMANDER 8A, 16A

627S, SA

CARTER WE

2002

1939

MODEL G

444S, 453S

CARTER WO

2012

1939 - 40

CHAMPION

A-19282 (6-91A)

STROMBERG BXV-25

2037

1939 - 40

CHAMPION

A-19272 (6-90)

STROMBERG BXV-2

2037

1940

COMMANDER

410S

CARTER WA-1

2011

1940

MODEL 26 CHAMPION

468S, SA

CARTER WO

2012

1941 - 45

CHAMPION

496S

CARTER WA-1

2038

1941 - 48

CHAMPION

380077 (6-100)

STROMBERG BXV-2

2037

1941 - 48

CHAMPION

380078 (6-101)

STROMBERG BXV-25

2037

1941 - 50

COMMANDER 11A, 12A, 14A, 15A, 16A, 17A

380036 (6-98A), 380178 (6-104D)

STROMBERG BXV-26

2037

1946 - 48

CHAMPION 5G, 6G, 7G

532S, 661S

CARTER WE

2002

1947 - 4S

G6

10562, A

ZENITH 28

2088

1949 - 52

CHAMPION 8G, 9G, 10G, 12G

715S

CARTER WE

2002

1949 - 52

CHAMPION

380283 (6-109)

STROMBERG BXV-26

2037

1950

COMMANDER 17A

627S, SA

CARTER WE

2002

1950 - 53

S17A DESERT

777S, SA

CARTER BBR1

2095

1953

CHAMPION 14G

989S, SA

CARTER WE

2002

1954

CHAMPION CUSTOM W1, F1

2190S

CARTER WE

2002

1954 - 56

CHAMPION 15G, 16G, 56G

2108S

CARTER WE

2002

1955 - 57

S17A DESERT

777S, SA

CARTER BBR1

2095

1956 - 58

CHAMPION 56G, 57G, 58G

2417S

CARTER WE

2002

1957 - 58

CHAMPION, SCOTSMAN

2724S, 2764S

CARTER BBR1

2080

1958

TAXI GY1, SCOTSMAN 58G

2808S

CARTER BBR1

2091

1960-62

LARK, TAXI 60S, 61S, 62S

2934S, SA, 3046S, SA, 3159S, 3160S, 3161S, 3186S, 3370S, 3371S, 3372S,

3373S

CARTER AS

2097

1965

194" ENG

7025087, 105, 108

ROCHESTER B, BC, BV

2046

1966

230" ENG

7026085

ROCHESTER B, BC, BV

2046

8 CYL

1932 - 33

PRESIDENT, 92

A-17002 (6-12)

STROMBERG EE-22

2041

1932 - 33

62-73, DICTATOR, COMMANDER

A-17022 (6-4)

STROMBERG EE-22

2041

1934

PRESIDENT C

A-17022 (6-4)

STROMBERG EE-22

2041

1935

"C" PRESIDENT, "B" COMMANDER

A-17661 (9-10)

STROMBERG EE-1

2039

1936

PRESIDENT

A-17921 (6-50), A-17931 (6-52)

STROMBERG EE-1

2039

1937

3-C

A-18401 (6-63)

STROMBERG EE-1

2039

1938 - 39

PRESIDENT 4C

A-18371 (6-70A)

STROMBERG AA0-161

2007

1940

PRESIDENT 7C

A-18611 (6-85)

STROMBERG AA0-161

2007

1940

PRESIDENT

409S

CARTER WDO

2055

1941 - 42

PRESIDENT 7C, 8C

380038 (6-97C)

STROMBERG AAV-26

2007

1951

(EARLY) "H" COMMANDER

380278 (6-107A)

STROMBERG AAUVB-26

2007

1951 - 52

(LATE) "H" COMMANDER

380313 (6-111A)

STROMBERG AAUVB-26

2007

1953 - 57

COMMANDER

6-112F, -113, -115A,-116, -117B, C

STROMBERG WW

2023

1955 - 60

CHAMPION, LARK, PRESIDENT, SCOTSMAN

2214S, SA, SB, 2219S, SA, SB, 2330S, SB, 2394S, 2574S, 2575S

CARTER WCFB

2022

1957 - 58

GOLDEN HAWK 57L, 57H-K7, 58H-K, -K7, -K9 W/SUPER CHARGER

6-121, A, B, C, 6-122A

STROMBERG WW

2100

1959 - 62

HAWK, LARK, CRUISFR

6-123, A, 6-125, 6-127, 6-128

STROMBERG WW

2023

1960 - 61

259", 289" ENG, LARK, HAWK

2829S, 2830S, 3165S, 3166S

CARTER WCFB

2004

1963 - 64

259", 289" ENG, DATONA, LARK, HAWK, SUPER JET AVANTI R2, 64VE JET

THRUST

3507S, 3588S, 3725S

CARTER AFB

2000

1963 - 64

CHALLENGER, CRUISER, COMMANDER, HAWK, LARK

6-130, 6-132

STROMBERG WW

2102

1963 - 64

259", 289" ENG

3506S, 3540S, 3589S, 3726S

CARTER AFB

2086

1964

304" ENG AVANTI-R3

3808S

CARTER AFB

2086

1964

304" ENG AVANTI R4 (2 CARBS)

3810S(F), 3811S(R)

CARTER AFB

2048

1965

283" ENG

7025186

ROCHESTER 4G, 4GC

5089A

1965

283" ENG

7024101, 110, 7025088

ROCHESTER 2G, 2GV

2043

6 CYL - TRUCK

1935 - 36

T2, T4, T6, T8, 2M2, 2T2

308S, 336S

CARTER W-1

2015

1937

J15, M, B, J20, M, MB

357S, 360S, 361S

CARTER W-1

2015

1937

J-30, J-30M

362S

CARTFR BB

2080

1938

K10, K15, K20, K25

360S, 361S, 394S, 395S

CARTER W-1

2015

1938 - 42

K10, K15, K20, K25

427S, 428S, 429S

CARTER BB

2080

1940 - 48

M16, M17

514S

CARTER BBR1

2080

1941 - 45

M5-M15

496S

CARTER WA-1

2038

1942 - 48

M5, M15, M16

380077 (6-100)

STROMBERG BXV-2

2037

1946 - 47

M5, M15

532S, 661S

CARTFR WE

2002

1947 - 48

M5, M15

10563, A

ZENITH 28

2088

1949 - 51

2R5, 2R10, 2R15

380282 (6-108)

STROMBERG BXOV-2

2307

1949 - 53

1/2 TON, 2R5, 2R10, 2R15

633S

CARTER BBR1

2080

1949 - 53

2R16, A, 2R17A, 11/2, 2TON

606S, SA, SB

CARTER BBR1

2095

1950 - 53

2R6, 2R11, 2R14

777S, SA

CARTER BBR1

2095

1955

1/2, 3/4, 1 TON

2125S

CARTER BBR1

2080

1956

2E6, 2E11, 2E14

777S, SA

CARTER BBR1

2095

1957

3E16, 3E17

605S, SA, SB

CARTER BBR1

2095

1957

3E6, 3E11, 3E14

777S, SA

CARTER BBRI

2095

1960

5E-6, -11, -14, -16

3062S, 3079S

CARTER AS

2098

1960 - 62

5E-5, 6E-5, 6E-10

2934S, SA, 3046S, SA, 3159S, 3160S, 3161S, 3162S, 3370S, 3371S, 3372S,

3373S

CARTER AS

2097

8 CYL - TRUCK

1955 - 59

- - - - -

2224S, 2575S

CARTER WCFB

2022

1955 - 62

ALL MODELS

6-114A, -115A, -118A, -119, -120, -123, A, -125, -126, A,

B, -127, -128, -129

STROMBERG WW

2023

1960 - 61

289" ENG 5E & 6E-13, -28, -40

2831S, 3167S

CARTER WCFB

2004

1963 - 64

8E7, 8E9, 8E12, 8E13, SE28, SE40

6-130, 6-131, 6-132, 6-133

STROMBERG WW

2102

Bob asked me about AFB non Avanti jet sizes.  Well I had old notes on

rod and jet sizes on the back of an IBM card (remember those?) stuck

into my parts book.  I added one or two fresh measurements.  So here is

what I have on rod/jet sizes:

Stude #   Application   Cruise   Power   Carter #

Std. AFB (non R-series)

1559343    3540 Std.     1.78     1.14   16-231

1559463    3540 1 lean   1.80     1.21   16-241

1559464    3540 2 lean   1.80     1.26   16-243

1562535    3726 Std.     1.74     1.42   16-98

1562536    3726 1 lean   1.74     1.46   16-294

1562537    3726 2 lean   1.76     1.48   16-296

Above with #537185 (120-159) (#43 drill) primary jet, except 16-296 is

used with (120-222) (#51 drill) primary jet (sold as a kit).

R-series:

1558398   3506/89 Std.    1.76     1.46   16-99

1559457   3506/89 1 lean  1.76     1.50   16-233

1560338   3507/88 Std.    1.94     1.25   16-263

1562539   3725 Std.       2.00     1.15   16-243

3506/89 use 537185 (120-159) (#43 drill) primary jet

3507/88 use 1549222 (120-162) (#39 drill) primary jet

3725 use 1550299 (120-224) primary jet

All metering rod measurements in mm.

--

wf.

Michael - Roseland FL wrote:

I have been trying different rod and jet combinations for some time now 
to try and get the R4 Avanti to run leaner and accelerate at the same 
time.  I have the correct number carter afb carbs. front and rear.  The 
rear carter does not use vacuum advance and Dave T. set my Chrysler 
converted electronic distributor up with centrifugal vs. vacuum advance 
as the rear carburetor does not have a vacuum advance pick up on an R4 from 
the factory. 

I bought a calibration kit from Summitt for a 500 CFM Edelbrock 
Performer.  Does anyone have any suggestions on the best size to use for 
rods and meters on this car?  Thanks!

R4 

      - Carter AFB 1-9/16" primaries, 1-11/16" secondaries 
            Front Carb 
            Standard model Stude# 1563051 
            AFB-3810S 
            flow 675 CFM (+-10) 
            Primary jet # 120-162 Size (0-1015) 
            Secondary Jet # 120-176 size (.0635) 
            Primary metering rod # 16-124 size (.069 X .0635) 
            float setting 5/16" 

            Rear Carb 
            Standard model Stude# 1563051 
            AFB-3811S 
            flow 675 CFM (+-10) 
            Primary jet # 120-162 Size (0-1015) 
            Secondary Jet # 120-122 size (.070) 
            Primary metering rod # 16-204 size (.073 X .063) 
            float setting 5/16" 

BobJ